## Slide 1
Subsurface Clean Energy Opportunities in the Pacific Northwest
& the Northwest Energy Shortfall
Annika Wallendahl | 11.5.2025
Geosyntec Consultants
Notes: Earth pattern

## Slide 2
Annika Wallendahl
Principal Engineer, PE, LG, MBA
Based in Seattle Office
Annika is a Principal Engineer with over 23 years experience. She is a leader in Geosyntec's nationwide energy transition, carbon advisory, and decarbonization teams. Annika is a licensed geologist and professional engineer in Washington State and supports clients across North America and Europe with planning and executing strategic decarbonization projects.
Notes: Right-click on the headshot and choose “Change Picture” to update the picture.

## Slide 3
About Geosyntec
Founded 1983 Employees 2,600+ worldwide
NORTH AMERICA
GLOBAL

## Slide 4
Northwest Energy Shortfall
Clean Energy Solutions
Agenda

## Slide 5: What is the Northwest Energy Shortfall?
Notes: Regional Energy Symposium held October 9 in Portland
Symposium convened over 300 energy leaders, legislators and energy industry experts
Symposium was kickoff for collaborative resource adequacy planning between natural gas and electricity providers
Expect rolling blackouts starting January 2026 across the Northwest on highest load days (coldest winter days)

## Slide 6: Energy Demand is Growing
NW energy demand expected to grow by 30% by 2030
Data center expansions are primary driver of load growth in region
Energy Production is Down
Hydroelectric generation down 24%
Fossil Fuel/Coal generation down due to retirements
Wholesale electricity generation blend relies on renewables – these don’t produce at nameplate capacity during cold snaps
Natural gas transmission and capacity is maxed on cold days

## Slide 7: 9 GW Energy Shortfall by 2030

## Slide 8: What Resources are Coming Online?
NW utilities to add 29 GW of new resources by 2035
  Mostly wind, solar, and battery resources
Battery energy storage system capacity projected to reach 18.8 GW by the end of 2025
  38% increase from the 13.6 GW at the end of 2024
Renewable resources perform poorly in extreme cold
  In bad conditions, 100 GW of nameplate capacity may produce <10 GW
Notes: *BESS capacity listed is for Western Electricity Coordinating Council (WECC) area (excluding California ISO)

## Slide 9: "Firm" Energy Resources are Needed
January 13-16, 2024 cold event exposed grid-wide vulnerability
Effective Load Carrying Capacity (ELCC%) is how a resource delivers during critical periods
NW needs to add more "firm" energy resources (high ELCC%)
Notes: Marginal ELCC (Effective Load Carrying Capability) is a method for assessing a power resource's contribution to grid reliability by measuring the incremental benefit of adding one more unit of that resource class to the system. This approach accounts for diminishing returns, meaning that the reliability contribution of each additional unit of a resource (like solar or battery storage) decreases as more of that same type of resource is added to the grid. This is in contrast to the average ELCC method, which considers the overall average contribution of all resources of that type.

## Slide 10: Clean Energy Resources are Reliable
Credit: WA DNR, The Washington Geothermal Experience

## Slide 11: Northwest Needs More Clean Energy
Development of emerging clean energy technologies to commercial/grid scale is still critical.
However, to end the Northwest energy shortfall, we need to add more:
  Distributed energy resources across the entire region
  Firm energy resources that can come online quickly
  Battery storage co-located with less firm energy resources
Also need to explore carbon management solutions, like subsurface carbon sequestration co-located with new fossil fuel/natural gas generating plants

## Slide 12: Subsurface Clean Energy Opportunities
Subsurface Opportunities
  Thermal Energy Storage & Networks
  Stimulated Geologic Hydrogen
  Shallow and Deep Geothermal
Image Credit: WA DNR
Notes: SB SB 6039 - 2023-24
Promoting the development of geothermal energy resources.
Agrivoltaics = 3.95 million amenable crop acres across WA State
https://energy.sandia.gov/programs/fossil-energy/subsurface-storage/geologic-hydrogen-capabilities/geologic-hydrogen/

## Slide 13
Why is
Low Temperature Geothermal
well suited to Washington?
Notes: Change text as needed – but keep short. To change the photo, move the filled rectangle over slightly, then right-click on the background photo and choose “Change Picture” to choose a theme-appropriate image. Move the transparent rectangle back in place.
The background photo has a translucent screen over it. To change, background photo move the translucent screen slightly to the left or right, then right-click on the background photo and choose “Change Picture and choose a new photo.

## Slide 14
Isabellah von Trapp
Senior Hydrogeologist, LHG
Based in Seattle Office
Isabellah is a licensed hydrogeologist who helps clients explore and develop the relationship between their water and energy systems. Her work includes water supply development, water rights permitting, aquifer characterization, as well as evaluating and implementing low temperature geothermal energy projects.
Notes: Right-click on the headshot and choose “Change Picture” to update the picture.

## Slide 15
Ground Source Heat Pumps
Washington Geology
Feasibility
Geothermal Definitions
Hydrogeology 101
The Future
Presentation Overview

## Slide 16
What Do We Mean By "Geothermal Energy"?
Geothermal energy works by harnessing heat from beneath the Earth's surface to generate electricity or provide heating and cooling, either through a direct heating system or a ground source heat pump.
LOW
MODERATE
HIGH
Ground Source Heat Pumps
Direct Use
Electricity Generation
300-700° F
45-75° F
75-250° F

## Slide 17
LOW
MODERATE
HIGH
Ground Source Heat Pumps
Direct Use
Electricity Generation
Geothermal energy works by harnessing heat from beneath the Earth's surface to generate electricity or provide heating and cooling, either through a direct heating system or a ground source heat pump.
45-75° F
What Do We Mean By "Geothermal Energy"?

## Slide 18
How Do Ground Source Heat Pumps Work?
Ground source heat pumps work by transferring energy between the ground and a building through borings or wells, using the Earth's stable underground temperature to efficiently heat and cool indoor spaces.
Closed-Loop
Open-Loop
Closed-Loop | Open-Loop
Can be installed anywhere No water right needed Large footprint required Significant costs at large-scale | Certain hydrogeologic conditions needed Water Right Permit / UIC Registration needed Smaller footprint required Economy of scale

## Slide 19
Why Are Aquifers Important in GSHP Design?
An aquifer is an underground layer of water-bearing material. Aquifer transmissivity is a measure of an aquifer’s ability to transmit groundwater.
Sand & Gravel
Fractured Bedrock
Water Pumped from Aquifer
Closed-Loop Design
Open-Loop Design

## Slide 20: Is a Feasibility Study Necessary?
Natural Groundwater Flow Direction
Induced Gradient from Pumping
85° F
40° F
Return Wells
Supply Wells
Thermal Energy Network
Vermont Community Thermal Networks
Temperature Impact Modeling
Notes: Add something about thermal energy network

## Slide 21
Selected technology to meet decarbonization goals
Centrally located within City limits
Constructed within past cleanup site (can be a constraint to UIC permitting)
Washington State Public Health Lab
Shoreline, Washington
Notes: Make text-heavy slides a white background

## Slide 22: What Have We Learned?
OPPORTUNITY

## Slide 23: Why Washington?
Washington Geological Survey, May 2024

## Slide 24
What’s NEXT ?

## Slide 25
Questions?
Ask Annika About:
Stimulated geologic hydrogen, carbon management, carbon sequestration
Ask Isabellah About: Ground source heat pump feasibility, design, permitting, construction
Annika Wallendahl
Annika.Wallendahl @Geosyntec.com
Isabellah von Trapp
Isabellah.vonTrapp @Geosyntec.com
Notes: Earth pattern